## Slide 1: TCP/IP Computer Networks Introduction to IP Networks
José Legatheaux Martins
Departamento de Informática da
FCT/UNL

## Slide 2: Lecture Outline
Basics
  Links and nodes
  Packets and multiplexing
IP service model
  Best-effort packet delivery
  Protocol layering in TCP/IP networks
  IP as the Internet’s “narrow waist”
IP packet structure
  Fields in the IP header
  How upper levels use and cooperate with the IP level
Using slides from the companion site of
  James F. Kurose and Keith W. Ross, “Computer Networking - A Top-Down Approach Featuring the Internet,” Addison Wesley
  Computer Networks, COS461, Jennifer Rexford, Princeton University, 2007 Edition

## Slide 3: Links: Delay and Bandwidth
Delay
  Time needed tp propagate data along the link
  Corresponds to the “length” of the link
  Typically measured in mili seconds
Bandwidth
  Amount of data sent (or received) per unit time
  Corresponds to the “width” of the link
  Typically measured in bits per second
bandwidth
delay
delay x bandwidth

## Slide 4: Connecting More Than Two Hosts
Multi-access link: Ethernet, wireless
  Single physical link, shared by multiple nodes
  Limitations on distance and number of nodes
Point-to-point links: e.g. fiber-optic cable
  Only two nodes (separate link per pair of nodes)
  Limitations on the number of adapters per node
multi-access link
point-to-point links

## Slide 5: Beyond Directly-Connected Networks
Switched network
  End hosts at the edge
  Network nodes that switch traffic
  Links between the nodes
Multiplexing
  Many end hosts communicate over the network
  Traffic shares access to the same links

## Slide 6: Packets
Data traffic divided into packets
  Each packet contains a header (with address)
Packets travel separately through network
  Packet forwarding based on the header
  Network nodes may store packets temporarily
Destination reconstructs the message

## Slide 7: Packet Switching: Statistical Multiplexing
Packets

## Slide 8: IP Service Model: Why Packets?
Data traffic is bursty
  Logging in to remote machines
  Exchanging e-mail messages
Don’t want to waste bandwidth
  No traffic exchanged during idle periods
Better to allow multiplexing
  Different transfers share access to same links
Packets can be delivered by almost anything
  RFC 1149: IP Datagrams over Avian Carriers (aka birds)
… still, packet switching introduces inefficiencies
  Extra header bits on every packet
  Flexibility compensates the overhead

## Slide 9: Why the Internet Protocol ?
Different (sub)networks had different options
  Packet formats
  Addresses
  Routing options
  Management and resource control
An interconnection layer
  Allows interoperation
  Hides specific network options

## Slide 10: IP Service: Best-Effort Packet Delivery
Packet switching
  Divide messages into a sequence of packets
  Headers with source and destination address
Best-effort delivery
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
source
destination
IP network

## Slide 11: IP Service Model: Why Best-Effort?
IP means never having to say you’re sorry…
  Don’t need to reserve bandwidth and memory
  Don’t need to do error detection & correction
  Don’t need to remember from one packet to next
Easier to survive failures
  Transient disruptions are okay during failover
… but, applications do want efficient, accurate transfer of data in order, in a timely fashion

## Slide 12: IP Service: Best-Effort is Enough
No error detection or correction
  Higher-level protocol can provide error checking
Successive packets may not follow the same path
  Not a problem as long as packets reach the destination
Packets can be delivered out-of-order
  Receiver can put packets back in order (if necessary)
Packets may be lost or arbitrarily delayed
  Sender can send the packets again (if desired)
No network congestion control (beyond “drop”)
  Sender can slow down in response to loss or delay

## Slide 13: Example: Transmission Control Protocol
Communication service (socket)
  Ordered, reliable byte stream
  Simultaneous transmission in both directions
Key mechanisms at end hosts
  Retransmit lost and corrupted packets
  Discard duplicate packets and put packets in order
  Flow control to avoid overloading the receiver buffer
  Congestion control to adapt sending rate to network load
source
network
destination
TCP connection

## Slide 14: Layering in the IP Protocols
Internet Protocol
Transmission Control
Protocol (TCP)
User Datagram
Protocol (UDP)
Telnet
HTTP
SONET
ATM
Ethernet
RTP
DNS
FTP

## Slide 15: The Internet Protocol Suite
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Waist
The waist facilitates interoperability
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…

## Slide 16: Layer Encapsulation
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B

## Slide 17: Is Layering Harmful?
Layer N may duplicate lower level functionality
  E.g., error recovery to retransmit lost data
Layers may need same information
  E.g., timestamps, maximum transmission unit size
Strict adherence to layering may hurt performance
  E.g., hiding details about what is really going on
Some layers are not always cleanly separated
  Inter-layer dependencies for performance reasons
  Some dependencies in standards (header checksums)
Headers start to get really big
  Sometimes more header bytes than actual content

## Slide 18: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 19: IP Header: Version, Length, ToS
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when “IP options” are used
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer

## Slide 20: IP Header: Length, Fragments, TTL
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 63,535 bytes (216 -1)
  … though underlying links may impose harder limits
Fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset
  Supports dividing a large IP packet into fragments
  … in case a link cannot handle a large IP packet
Time-To-Live (8 bits)
  Used to identify packets stuck in forwarding loops
  … and eventually discard them from the network

## Slide 21: IP Header: To and From Addresses
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique identifier for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique identifier for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source

## Slide 22: Source Address: What if Source Lies?
Source address should be the sending host
  But, who’s checking, anyway?
  You could send packets with any source you want
Why would someone want to do this?
  Launch a denial-of-service attack
    Send excessive packets to the destination
    … to overload the node, or the links leading to the node
  Evade detection by “spoofing”
    But, the victim could identify you by the source address
    So, you can put someone else’s source address in the packets
  Also, an attack against the spoofed host
    Spoofed host is wrongly blamed
    Spoofed host may receive return traffic from the receiver

## Slide 23: Protocol Demultiplexing
Multiple choices at each layer
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
TCP/UDP
IP
Port Number
Network
Protocol Field
Type Field

## Slide 24: Resource Allocation: Queues
Sharing access to limited resources
  E.g., a link with fixed service rate
Simplest case: first-in-first out queue
  Serve packets in the order they arrive
  When busy, store arriving packets in a buffer
  Drop packets when the queue is full

## Slide 25: Resource Allocation: Congestion Control
What if too many folks are sending data?
  Senders agree to slow down their sending rates
  … in response to their packets getting dropped
The essence of TCP congestion control
  Key to preventing congestion collapse of the Internet

## Slide 26: Transmission Control Protocol
Flow control: window-based
  Sender limits number of outstanding bytes (window size)
  Receiver window ensures data does not overflow receiver
Congestion control: adapting to packet losses
  Congestion window tries to avoid overloading the network (increase with successful delivery, decrease with loss)
  TCP connection starts with small initial congestion window
time
congestion window
slow start
congestion avoidance

## Slide 27: History
IP proposed in the early 1970s
  Defense Advanced Research Project Agency (DARPA)
Goal: connect existing networks
  To develop an effective technique for multiplexed utilization of existing interconnected networks
  E.g., connect packet radio networks to the ARPAnet
Motivating applications
  Remote login to server machines
  Inherently bursty traffic with long silent periods

## Slide 28: Other Main Driving Goals (In Order)
Communication should continue despite failures
  Survive equipment failure or physical attack
  Traffic between two hosts continue on another path
Support multiple types of communication services
  Differing requirements for speed, latency, & reliability
  Bidirectional reliable delivery vs. message service
Accommodate a variety of networks
  Both military and commercial facilities
  Minimize assumptions about the underlying network

## Slide 29: Other Driving Goals, (Not ?) Met
Permit distributed management of resources
  Nodes managed by different institutions
  … though this is still rather challenging
Cost-effectiveness
  Statistical multiplexing through packet switching
  … though packet headers and retransmissions wasteful
Ease of attaching new hosts
  Standard implementations of end-host protocols
  … though still need a fair amount of end-host software
Accountability for use of resources
  Monitoring functions in the nodes
  … though this is still fairly limited and immature

## Slide 30: The Landscape is Changing
The Internet is increasingly becoming an pervasive heterogeneous network
The edge will become predominantly mobile
Multi-point communication paradigms are emergent
Security and malicious communication patterns abounding
Researchers have identified several architectural obstacles
  Addresses and identifiers
  Security
  Layering
  Services and protocols
  Resource usage and billing

## Slide 31: Drawbacks — The Price of Success
The security and authorization models are too naïve
  and are showing their limitations
Mobility and multi-point diffusion are difficult to deal with
  addresses, identifiers, transport protocols, …
Many new applications and protocols require new ways to deal with layering
  Overlay networks are just a short term solution ?
Resource usage and billing models are also showing some limitations
  Service providers do not know how to bill new services

## Slide 32: Paths to the Future
Current Internet is basically flawed — one should build a new one
  Clean slate approach
Current Internet cannot be abruptly replaced. We must proceed studying alternatives subject to real users, applications and load
  Evolutionary approach

## Slide 33: Conclusion
Success
  Packet switching
  Layering,
  Best effort model,
  End-to-end principles
  Support of heterogeneity, several types of links, …
  Multiple services,
  Scale
Problems
  Security,
  Management,
  Layering and adaptability,
  End-to-end principles
  Resource usage model

## Slide 34: Written assignment
Each student must produce a written report of at most 5 pages (12 dots, double spaced) on the subject of one of the following papers:
  J. Saltzer, D. Reed ad D. Clark, “End-to-End Arguments in System Design,” ACM Transactions on Computer Systems (4):277-288, November 1984
Deliver date: in the class of September, 18 th