## Slide 1: TCP/IP Computer Networks Performance Metrics
José Legatheaux Martins
Departamento de Informática da
FCT/UNL

## Slide 2: Lecture Outline
Queuing Model
Generic Performance Metrics
Components of Hop and End-to-End Packet Delay
More Performance Measures
Tools
Using slides from the companion site of
  James F. Kurose and Keith W. Ross, “Computer Networking - A Top-Down Approach Featuring the Internet,” Addison Wesley

## Slide 3: Computer Networks
12
1
11
8
4
7
2
6
9
10
14
5
13
15
3
Host
B
Host
C
Host
L
Host
D
Host
E
Host
G
Host
J
Host
A
Host
H
Host
F
Host
M
16
17
W
T
X
Y
Z
nodes
AP
W1
W2
W3
W4
links

## Slide 4: Link Performance Measures
Throughput or link capacity - bits/sec. successfully sent [e.g. Throughput = 10 Mbps]
Error rate – the fraction of bits correctly received over sent ones [e.g. Error rate = 10-9]
Propagation delay — time a bits takes to travel across the link [e.g. Prop. delay = 10 ms]
Link utilization - the average fraction of time a link is busy [e.g. Utilization = 0.8]
  when overhead is taken into account (i.e., it is excluded from the useful bits sent), link utilization is often referred to as link efficiency.

## Slide 5: Simple Queuing Model
Customer
Arrivals
Queue
Server

## Slide 6: Router Node
packet
node
Outgoing Link
Router Buffer
Server
packet
Incoming Link

## Slide 7
Utilization (taxa de utilização)
  the percentage of time a device is busy servicing a “customer”.
Throughput (desempenho)
  the number of jobs processed by the “system” per unit time.
Response time (tempo de resposta)
  the time required to receive a response to a request (round-trip time (RTT) ).
Delay (atraso)
  the time to traverse from one end to the other of a system.
Queuing Metrics

## Slide 8: End-to-End Packet Delay
End-to-end delay includes multiple hop link delays.

## Slide 9: Hop Delay Components
A
B
propagation
transmission
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop

## Slide 10: Nodal Delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 11: Queuing Delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queuing delay small
La/R -> 1: delays become large
La/R = or > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 12: Implementation: Packet drop
Queue (aka buffer) preceding link in buffer has finite capacity.
Packet arriving to full queue is dropped (aka lost) [FIFO Drop Tail router].
Lost packet may be retransmitted by previous node, by source end system, or not at all.
B
packet being transmitted
packet arriving to
full buffer is dropped.
buffer
(waiting area)
A

## Slide 13: Network Path Performance Measures
End-to-end delay
  Delay from source to destination. Measured from when the sender starts sending a packet up to when the receiver completely receives the packet
Latency
  Usually implies the minimum possible delay. Latency assumes no queuing and no contention encountered along the path.
Jitter
  Variance of end-to-end delay.

## Slide 14: More
Packet loss rate
  the percentage of packets lost or dropped.
Goodput
  {measured at the receiver} The rate in bits per second of useful traffic received. Goodput excludes duplicate packets and packets dropped along the path.
Fairness
  either Jain’s fairness or max-min fairness are used to measure fair treatment among competing flows.
Quality of Service (QoS)
  a QoS measure accounts for importance of specific metric to one type of application [e.g. jitter and playable frame rate for streaming media].

## Slide 15: Throughput / Goodput
throughput — rate (bits/time unit) at which bits are transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 16: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 17: Throughput: Internet Scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often the bottleneck
The last mile link has capacity Rc.

## Slide 18: Wireless Links Performance Metrics
WLANs and WSNs are very concerned with
packet loss and employ additional metrics:
Delivery ratio
  the ratio of packets received to packets sent {excluding duplicates and retransmissions}.
Link layer retransmission rates
  the percentage of DL layer frames that are retransmitted.

## Slide 19: Tools
Useful tools:
    Ping
    iperf
    Traceroute
    tcpdump
    wireshark
    and many others
Look into Wikipedia

## Slide 20: Performance Metrics Summary
The three most general performance measures are : utilization, throughput and response time.
In computer networks, end-to-end delay is an important performance metric.
Queuing models are used to analyze and estimate computer network performance.
Other useful metrics include: latency, goodput, fairness and QoS metrics such as jitter.
In wireless networks, delivery ratio, packet loss rate and link layer retransmission rates are valuable network measures.