## Slide 1: TCP/IP Computer Networks Link Layer Issues and Multiple Access Protocols Examples
José Legatheaux Martins
Departamento de Informática da
FCT/UNL

## Slide 2: Lecture Outline
Link-layer services
Sharing a shared media
Ethernet protocol
  Carrier sense, collision detection, and random access
  Frame structure
  Hubs and switches
Token Ring protocol
  The coordination algorithm
  Characteristics
Using some slides from the companion sites of
  James F. Kurose and Keith W. Ross, “Computer Networking - A Top-Down Approach Featuring the Internet,” Addison Wesley
  Computer Networks, COS461, Jennifer Rexford, Princeton University, 2007 Edition

## Slide 3: Adaptors Communicating
Link layer implemented in adaptor (network interface card)
  Ethernet card, 802.11 card
Sending side:
  Encapsulates datagram in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
datagram
frame
adapter
adapter
link layer protocol

## Slide 4: Link-Layer Services
Encoding
  Representing the 0s and 1s
Framing
  Encapsulating packet into frame, adding header, trailer
  Using MAC addresses, rather than IP addresses
Error detection
  Errors caused by signal attenuation, noise.
  Receiver detecting presence of errors
Error correction
  Receiver correcting errors without retransmission
Flow control
  Pacing between adjacent sending and receiving nodes

## Slide 5: Encoding
Signals propagate over physical links
  Source node encodes the bits into a signal
  Receiving node decodes the signal back into bits
Simplify some electrical engineering details
  Assume two discrete signals, high and low
  E.g., could correspond to two different voltages
Simple approach
  High for a 1, low for a 0
0 0 1 1 0 0 1 1 0 0 0 1 1 1 1 1 0 0

## Slide 6: Problem With Simple Approach
Long strings of 0s or 1s introduce problems
  No transitions from low-to-high, or high-to-low
Receiver keeps average of signal it has received
  Uses the average to distinguish between high and low
  Long flat strings make receiver sensitive to small change
Transitions also necessary for clock recovery
  Receiver uses transitions to drive its own clock
  Long flat strings do not produce any transitions
  Can lead to clock drift at the receiver
Alternatives (see Section 2.2)
  Non-return to zero inverted, and Manchester encoding

## Slide 7: Manchester encoding
Used in 10BaseT
Each bit has a transition
Allows clocks in sending and receiving nodes to synchronize to each other
  no need for a centralized, global clock among nodes!

## Slide 8: Framing
Break sequence of bits into a frame
  Typically implemented by the network adaptor
Sentinel-based or Flag-based (also used in byte-oriented protocols)
  Delineate frame with special pattern (e.g., 01111110)
  Problem: what if special patterns occurs within frame?
  Solution: escaping the special characters
    E.g., sender always inserts a 0 after five 1s
    … and receiver always removes a 0 appearing after five 1s
01111110
01111110
Frame contents

## Slide 9: Framing (Continued)
Physical layer-based
  With some forms of encoding (e.g. Used in several links at the physical layer) it is possible to encode a flag as a special signal, different from any signal encoding data
Counter-based (in fact similar to flag-based)
  Include the payload length in the header
  … instead of putting a sentinel at the end
  Problem: what if the count field gets corrupted?
    Causes receiver to think the frame ends at a different place
  Solution: catch later when doing error detection
    And wait for the next flag for the start of a new frame

## Slide 10: Error Detection
Errors are unavoidable
  Electrical interference, thermal noise, etc.
Error detection
  Transmit extra (redundant) information
  Use redundant information to detect errors
  Extreme case: send two copies of the data
  Trade-off: accuracy vs. overhead
Techniques for detecting errors
  Parity checking
  Checksum
  Cyclic Redundancy Check (CRC)

## Slide 11: Error Detection Techniques
Parity check
  Add an extra bit to a 7-bit code
  Odd parity: ensure an odd number of 1s
    E.g., 0101011 becomes 01010111
  Even parity: ensure an even number of 1s
    E.g., 0101011 becomes 01010110
Checksum
  Treat data as a sequence of 16-bit words
  Compute a sum of all the 16-bit words, with no carries
  Transmit the sum along with the packet
Cyclic Redundancy Check (CRC)
  See Section 2.4 of Chapter 2

## Slide 12: Point-to-Point vs. Broadcast Media
Point-to-point
  PPP for dial-up access
  Point-to-point link between Ethernet switch and host
  Most long distance channels sold by carriers and telecom operators
Broadcast (shared wire or medium)
  Traditional Ethernet
  802.11 wireless LAN
  Token Ring

## Slide 13: Broadcast Media Based Links
May use guided (“wires”) or unguided propagation media (“space”)
The offered service is the best-effort transmission of point-to-point or multi-point transmission of frames (“unicasting”, “broadcasting” and “multicasting”)
In unguided media with an high error rate, the physical layer attempts to correct transmission errors (“forward error correction”).

## Slide 14: Multiple Access Protocol
Single shared broadcast channel
  Avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
Multiple access protocol
  Distributed algorithm for sharing the channel
  Algorithm determines which node can transmit
Classes of techniques
  Channel partitioning: divide channel into pieces
  Taking turns: passing a token for the right to transmit
  Random access: allow collisions, and then recover

## Slide 15: The Ideal Multiple Access Protocol
A link with a R bps bit data rate and being used by N nodes
  If just one node needs to communicate, then it should be allowed to use all the transmission capacity (R)
  If N nodes are transmitting, then, in average, each should be able to use R / N bps
  The protocol is simple and fully decentralized

## Slide 16: Three Ways to Share the Media
Channel partitioning MAC protocols
  Share channel efficiently and fairly at high load
  Inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  Efficient at low load: single node can fully utilize channel
  High load: collision overhead
“Taking turns” protocols
  Eliminates empty slots without causing collisions
  Vulnerable to failures (e.g., failed node or lost token)

## Slide 17: Random Access Protocols
When node has a packet to send
  Transmits it at full channel data rate R
  No a priori coordination among nodes
Two or more transmitting nodes ➜ “collision”,
Random access MAC protocol specifies:
  How to detect collisions
  How to recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 18: Ethernet
Dominant wired LAN technology:
First widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10 Mbps – 10 Gbps (100 Gbps expected soon)
Metcalfe’s
Ethernet
sketch

## Slide 19: CSMA Collisions
Collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission
Collision:
entire packet transmission
time wasted

## Slide 20: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection
  Easy in wired LANs: measure signal strengths, compare transmitted, received signals
  Difficult in wireless LANs: receiver shut off while transmitting
Human analogy: the polite conversationalist

## Slide 21: CSMA/CD Collision Detection

## Slide 22: Ethernet Uses CSMA/CD
Carrier sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
Collision detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random access: exponential back-off
  After collision, wait a random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again

## Slide 23: Ethernet Algorithm
A: sense channel, if idle
  then {
  transmit and monitor the channel;
      If detect another transmission
      then {
      abort and send jam signal;
        update # collisions;
        delay as required by exponential back-off algorithm;
        goto A
        }
      else {done with the frame; set collisions to zero}
    }
  else {wait until ongoing transmission is over and goto A}

## Slide 24: Sharing the Media
CSMA - Carrier Sense Multiple Access
CD - Collision Detection
Frame
Idle period
Contention period
Transmission period
Contention slots
Frame
Frame
Frame

## Slide 25: Collisions and latency
A
B
A
B
A
B
A
B
Time
t
t+d
t+2d
B detects the collision and sends jamming signal B
Finally A detects the collision
d - worst case transmission path delay

## Slide 26: Limitations on Ethernet Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions on Ethernet, according to the standard:
  Maximum length of the wire: 2500 meters
  Minimum length of the packet: 512 bits (64 bytes)
latency d
A
B

## Slide 27: Collision slot and the smallest frame
These slots are called collision windows or collision slots
According to the IEEE 802.3 standard, the collision slot is 51.2 micro seconds at 10 Mbps. According to the standard, the network should have at most 2500 meters
In a 10 Mbps Ethernet, the collision slot allows the transmission of 512 bits
In a 100 Mbps Ethernet the collision slot is 5.12 micro seconds, the maximum size is 200 meters and the minimal frame also has 512 bits or 64 bytes
For compatible reasons, all different Ethernet technologies kept the minimal and maximal byte sizes of the frame

## Slide 28: Exponential Back-off
Goal: to adapt the delay, before transmitting after a collision, to the link load
First collision: choose K randomly from {0,1}; delay = 0 or 512 bit transmission times
Second collision: choose K randomly from {0,1,2,3}…
After 10 or more collisions: choose K randomly from {0,1,2,3,4,…,1023}....
After 10 iterations without being able to transmit, abort

## Slide 29: CSMA/CD efficiency
Tprop = max prop between 2 nodes in LAN
ttrans = time to transmit max-size frame
Efficiency goes to 1 as tprop goes to 0
Goes to 1 as ttrans goes to infinity
Decentralized, simple, and cheap

## Slide 30: Ethernet Frame Structure
Sending adapter encapsulates packet in frame
Preamble: synchronization
  Seven bytes with pattern 10101010, followed by one byte with pattern 10101011
  Used to synchronize receiver, sender clock rates

## Slide 31: Ethernet Frame Structure (Continued)
Addresses: source and destination MAC addresses
  Adaptor passes frame to network-level protocol
    If destination address matches the adaptor
    Or the destination address is the broadcast address
    Or the destination address is one of the multicast addresses of the adaptor
    Or the adaptor is in “promiscuous” mode
  Otherwise, adapter discards frame
Type: indicates the higher layer protocol
  Usually IP
  But also Novell IPX, AppleTalk, …
CRC: cyclic redundancy check
  Checked at receiver
  If error is detected, the frame is simply dropped

## Slide 32: Frame Fields Sizes in Bytes
Checksum
Pading
Data
Data length or protocol
Preamble
Source and destination addresses
Start of
frame
Bytes
7
1
6
6
2
0 a 1500
0 a 46
4

## Slide 33: Hubs: Physical-Layer Repeaters
Hubs are physical-layer repeaters
  Bits coming from one link go out all other links
  At the same rate, with no frame buffering
  No CSMA/CD at hub: adapters detect collisions
twisted pair
hub

## Slide 34: Interconnecting with Hubs
Backbone hub interconnects LAN segments
All packets seen everywhere, forming one large collision domain
Can’t interconnect Ethernets of different speeds
hub
hub
hub
hub

## Slide 35: Ethernet Evolution: Switch
Link layer device
  Stores and forwards Ethernet frames
  Examines frame header and selectively forwards frame based on MAC dest address
  When frame is to be forwarded on segment, uses CSMA/CD to access segment
Transparent
  Hosts are unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured

## Slide 36: Switch: Traffic Isolation
Switch breaks subnet into LAN segments
Switch filters packets
  Same-LAN-segment frames not usually forwarded onto other LAN segments
  Segments become separate collision domains
hub
hub
hub
switch
collision domain
collision domain
collision domain

## Slide 37: Benefits of Ethernet
Easy to administer and maintain
Inexpensive
Increasingly higher speed
Moved from shared media to switches
  Change everything except the frame format
  A good general lesson for evolving the Internet

## Slide 38: Taking Turns MAC Protocols
Nodes perform a distributed algorithm to coordinate which one can transmit next
Most algorithms are based on a ring (“Token Ring”, FDDI, ...) or on polling by a central arbiter
There is an alternative based on a logical ring (“Token Bus”) and bus physical configuration as the Ethernet
Most of these solutions do not enjoy nowadays a wide deployment

## Slide 39: Ring Paradigm
Logical (and physical) ring allowing frames to visit all nodes

## Slide 40: Node active or bypassed

## Slide 41: Multistation Access Unit

## Slide 42: Token Ring MAC
free token

## Slide 43: Token Ring MAC
busy token
data
data
data
data
Sending
node
Receiver
node

## Slide 44: Token Ring MAC
free token
Sending
node

## Slide 45: Final Comments
This MAC protocol insures a fair sharing of the link and a bounded delay before each node is able to transmit
When facing high load, the protocol overhead is smaller than the one of Ethernet
However, all rings require rather complex interfaces because the ring must be managed to avoid lost or corrupted tokens and other forms of malfunction

## Slide 46: Conclusions
Link layer performs key services
  Encoding, framing, and error detection
  Optionally error correction and flow control
Shared media introduce interesting challenges
  Decentralized control over resource sharing
  Partitioned channel, taking turns, and random access
  Ethernet as a wildly popular example