## Slide 1: TCP/IP Computer Networks Ethernet Switching
José Legatheaux Martins
Departamento de Informática da
FCT/UNL

## Slide 2: Lecture Outline
Switch protocols and mechanisms
  Self learning of the switch table
  Spanning trees
Spanning Tree Protocol
Spanning Trees and Virtual LANs (VLANs)
Using some slides from the companion site of
  James F. Kurose and Keith W. Ross, “Computer Networking - A Top-Down Approach Featuring the Internet,” Addison Wesley
  Computer Networks, COS461, Jennifer Rexford, Princeton University, 2007 Edition

## Slide 3: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub

## Slide 4: Link Layer: Switches
Typically connects individual computers or other switches
  A switch is essentially the same as a bridge
  … though typically used to connect hosts, not LANs
Support concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D

## Slide 5: Dedicated Access and Full Duplex
Dedicated access
  Host has direct connection to the switch
  … rather than a shared LAN connection
Full duplex
  Each connection can send in both directions
  Host sending to switch, and host receiving from switch
  E.g., in 10BaseT and 100Base T
Completely avoids collisions
  Each connection is a bidirectional point-to-point link
  No need for carrier sense, collision detection, and so on, and no intrinsic distance limitation due to propagation delay

## Slide 6: Bridges/Switches: Traffic Isolation
Switch breaks subnet into LAN segments
  Segments become separate collision domains
Switch filters packets
  Frames are only forwarded to the necessary segments
hub
hub
hub
switch/bridge
collision domain
collision domain
collision domain

## Slide 7: Motivation For Self Learning
Switches forward frames selectively
  Forward frames only on segments that need them
Switch table
  Maps destination MAC address to outgoing interface
  Goal: construct the switch table automatically
switch
A
B
C
D

## Slide 8: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a time-to-live field to eventually forget the mapping
A
B
C
D
Switch learns how to reach A.

## Slide 9: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often
A
B
C
D
When in doubt, shout
(flood) !

## Slide 10: Switch Filtering/Forwarding
When switch receives a frame:
index switch table using MAC dest address
if entry found for destination then{
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 11: TTL Timers
When entries are stored in the “Switching tables”; TTL timers control the time they are allowed in the table (if not refreshed)
  This avoids switching tables growing uselessly for ever
  Eases the management of small switching tables
  Can the same address be associated with different ports ?

## Slide 12: Characteristics of switches
If the network only uses switches, all links are point-to-point, full-duplex and, therefore, there are no collisions
As switches are store & forward devices, there may have ports at different speeds
Routing is based on (“flooding”) optimized by self-learning filtering tables (“backward learning”)
As long as there are no cycles, the network scales
However, it still is as easy to manage as a shared link
The biggest limitation is related with the use of “flooding”

## Slide 13: Flooding Can Lead to Loops
Switches sometimes need to broadcast frames
  Upon receiving a frame with an unfamiliar destination
  Upon receiving a frame sent to the broadcast address
Broadcasting is implemented by flooding
  Transmitting frame out every interface
  … except the one where the frame arrived
Flooding can lead to forwarding loops
  E.g., if the network contains a cycle of switches
  Either accidentally, or by design for higher reliability

## Slide 14: Solution: Spanning Trees
Ensure the topology has no loops
  Avoid using some of the links when flooding
  … to avoid forming a loop
Spanning tree
  Sub-graph that covers all vertices but contains no cycles
  Links not in the spanning tree do not forward frames

## Slide 15: Broadcast Spanning Tree
A
B
G
D
E
c
F
A
B
G
D
E
c
F
A sends a frame
D sends a frame
First, build the spanning tree
Then, use it to bi-directionally diffuse frames from any source

## Slide 16: Constructing a Spanning Tree
Need a distributed algorithm
  Switches cooperate to build the spanning tree
  … and adapt automatically when failures occur
Key ingredients of the algorithm
  Switches need to elect a “root”
    The switch with the smallest identifier
  Each switch identifies if its interface is on the shortest path from the root
    And it exclude from the tree if not
  Messages (Y, d, X)
    From node X
    Claiming Y is the root
    And the distance is d
root
One hop
Three hops

## Slide 17: Steps in Spanning Tree Algorithm
Initially, each switch thinks it is the root
  Switch sends a message out every interface
  … identifying itself as the root with distance 0
  Example: switch X announces (X, 0, X)
Switches update their view of the root
  Upon receiving a message, check the root id
  If the new id is smaller, start viewing that switch as root
Switches compute their distance from the root
  Add K to the distance received from a neighbor
  Identify interfaces not on a shortest path to the root
  … and exclude them from the spanning tree

## Slide 18: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 19: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 20: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
    Need to elect a new root, with the next lowest identifier
  Failure of other switches and links
    Need to recompute the spanning tree
Root switch continues sending messages
  Periodically reannouncing itself as the root (1, 0, 1)
  Other switches continue forwarding messages
Detecting failures through timeout (soft state!)
  Switch waits to hear from others
  Eventually times out and claims to be the root
See Section 3.2.2 in the textbook for details and another example

## Slide 21: STP Frames
Protocol Identifier (2 bytes)
Version (1 byte)
Message Type (1 byte)
Flags (1 byte) — Topology Change Bit, ACK Bit
Root ID (8 bytes) — 2 byte priority (0x8000 by default) + 6 bytes (Mac Address)
Root Path Cost (4 bytes)
Bridge ID (8 bytes) — Sender ID
Port ID (2 bytes) — 1 byte with priority + 1 byte with port number
Message Age (2 bytes) — Message age since it has been sent by the root 1/256 s
Maximum Age (2 bytes) — If root messages are not detect since it, start reconfiguration
Hello Time (2 bytes) — Period between to hello root messages (default is 2 s)
Forward Delay (2 bytes) — Time needed to switch a port from blocked to active (default is 15 s)
4
2
2
2
2
2
2
8
8
1
1
1

## Slide 22: Evolution Toward Virtual LANs
In the olden days…
  Thick cables snaked through cable ducts in buildings
  Every computer they passed was plugged in
  All people in adjacent offices were put on the same LAN
  Independent of whether they belonged together or not
More recently…
  Switches changed all that
  Every office connected to central wiring closets
  Often multiple LANs (k hubs) connected by switches
  Flexibility in mapping offices to different LANs
Group users based on organizational structure, rather than the physical layout of the building.

## Slide 23: Why Group by Organizational Structure?
Security
  Ethernet is a shared media
  Any interface card can be put into “promiscuous” mode
  … and get a copy of all of the traffic
  So, isolating traffic on separate LANs improves security
Load
  Some LAN segments are more heavily used than others
  E.g., researchers running experiments get out of hand
  … can saturate their own segment and not the others
  Plus, there may be natural locality of communication
  E.g., traffic between people in the same research group

## Slide 24: People Move, and Roles Change
Organizational changes are frequent
  E.g., faculty office becomes a grad-student office
  E.g., graduate student becomes a faculty member
Physical rewiring is a major pain
  Requires unplugging the cable from one port
  … and plugging it into another
  … and hoping the cable is long enough to reach
  … and hoping you don’t make a mistake
Would like to “rewire” the building in software
  The resulting concept is a Virtual LAN (VLAN)

## Slide 25: Example: Two Virtual LANs
Red VLAN and Orange VLAN
Bridges forward traffic as needed
R
RO
RO
O
RO

## Slide 26: Example: Two Virtual LANs
Red VLAN and Orange VLAN
Switches forward traffic as needed
R
O
RO
R
R
R
O
O
O
R
O
R
R
R
O
O
O

## Slide 27: Making VLANs Work
Bridges/switches need configuration tables
  Saying which VLANs are accessible via which interfaces
Approaches to mapping to VLANs
  Each interface has a VLAN color
    Only works if all hosts on same segment belong to same VLAN
  Each MAC address has a VLAN color
    Useful when hosts on same segment belong to different VLANs
    Useful when hosts move from one physical location to another
Changing the Ethernet header
  Adding a field for a VLAN tag
  Implemented on the bridges/switches
  … but can still interoperate with old Ethernet cards

## Slide 28: Making VLANs Work (continued)
The VLANs standard: 802.1Q
The Spanning Tree Protocol Standard: 802.1D
  Each VLAN has its own Spanning Tree
VLANS can be interconnected by routers

## Slide 29: Scalable Switched Networks
Full-duplex high-speed fiber links over long distances are becoming cheaper
Switched networks are easy to manage and could span very large areas, however they are too limited in the number of hosts they are able to interconnect
  Using broadcasting limits the size of the network
  Multicasting also require switches to flood frames
Much work is being pursued to improve switching networks
  Spanning trees per VLAN and Pruned Spanning Trees
  Improved versions of the Spanning Tree Protocol
  Link aggregation and load balancing
  IGMP snooping
  ARP and DHCP Proxies
  Software Defined Networks (starting being used in data centers)

## Slide 30: Conclusion
Shuttling data from one link to another
  Bits, frames, packets, …
  Repeaters/hubs, bridges/switches, routers, …
Key ideas in switches
  Cut-through switching
  Self learning of the switch table
  Spanning trees
  Virtual LANs (VLANs)

## Slide 31: Optional Reading
  Radia Perlman, “An Algorithm for Distributed Computation of Spanning Trees in a Extended LAN,” Proceedings of the 9th Data Communications Symposium, pp. 124-133, September 1985