## Slide 1: TCP/IP Computer Networks Internet Addresses and Routing
José Legatheaux Martins
Departamento de Informática da
FCT/UNL

## Slide 2: Lecture Outline
Address allocation
  Classful addresses
  Classless InterDomain Routing (CIDR)
  Growth in the number of prefixes over time
Packet forwarding
  Forwarding tables
  Longest-prefix match forwarding
  Where forwarding tables come from
Using slides from the companion sites of
  James F. Kurose and Keith W. Ross, “Computer Networking - A Top-Down Approach Featuring the Internet,” Addison Wesley
  Computer Networks, COS461, Jennifer Rexford, Princeton University, 2007 Edition

## Slide 3: IP Address (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation
00001100
00100010
10011110
00000101
12
34
158
5

## Slide 4: Hierarchical Addressing: IP Prefixes
Divided into network & host portions (left and right)
12.34.158.0/24 is a 24-bit prefix with 28 addresses
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5

## Slide 5: IP Address and a 24-bit Subnet Mask
00001100
00100010
10011110
00000101
12
34
158
5
11111111
11111111
11111111
00000000
255
255
255
0
Address
Mask

## Slide 6: Address Allocation
How to assign address to organizations ?

## Slide 7: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
  Class B: 10*
    Large /16 blocks (e.g,. FCCN has 193.136.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., FCT/UNL had 193.136.122.0/24)
  Class D: 1110*
    Multicast groups
  Class E: 11110*
    Reserved for future use
This is why folks use dotted-quad notation!

## Slide 8: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15

## Slide 9: Examples
Several /16 blocks aggregated
  FCCN has 193.136.0.0/15
  193.136.0.0/16 and 193.137.0.0/16
FCT/UNL has the equivalent to 8 old class Cs aggregated
  FCT/UNL has 193.136.120.0/21
  193.136.0.0/24 to 193.136.0.7/24

## Slide 10: CIDR: Hierarchal Address Allocation
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.64.0/19
12.253.96.0/19
12.253.128.0/19
12.253.160.0/19
:
:
:
Prefixes are key to Internet scalability
  Address allocated in contiguous chunks (prefixes)
  Routing protocols and packet forwarding based on prefixes
  Today, routing tables contain ~500,000 prefixes

## Slide 11: Scalability: Address Aggregation
Provider is given 201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider
Routers in the rest of the Internet just need to know how to reach 201.10.0.0/21. The provider can direct the IP packets to the appropriate customer.

## Slide 12: But, Aggregation Not Always Possible
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homed customer with 201.10.6.0/23 has two providers. Other parts of the Internet need to know how to reach these destinations through both providers.

## Slide 13: Scalability Through Hierarchy
Hierarchical addressing
  Critical for scalable system
  Don’t require everyone to know everyone else
  Reduces amount of updating when something changes
Non-uniform hierarchy
  Useful for heterogeneous networks of different sizes
  Initial class-based addressing was far too coarse
  Classless InterDomain Routing (CIDR) helps

## Slide 14: Obtaining a Block of Addresses
Separation of control
  Prefix: assigned to an institution
  Addresses: assigned by the institution to their nodes
Who assigns prefixes?
  Internet Corporation for Assigned Names and Numbers
    Allocates large address blocks to Regional Internet Registries
  Regional Internet Registries (RIRs)
    E.g., RIPE (Réseaux IP Européens)
    Allocates address blocks within their regions
    Allocated to Internet Service Providers and large institutions
  Internet Service Providers (ISPs)
    Allocate address blocks to their customers
    Who may, in turn, allocate to their customers…

## Slide 15: Figuring Out Who Owns an Address
Address registries
  Public record of address allocations
  Internet Service Providers (ISPs) should update when giving addresses to customers
  However, records are notoriously out-of-date
Ways to query
  UNIX: “whois –h whois.ripe.net 193.136.122.0”
  http://www.ripe.net/whois/
  http://www.geektools.com/whois.php
  …

## Slide 16: Are 32-bit Addresses Enough?
Not all that many unique addresses
  232 = 4,294,967,296 (just over four billion)
  Plus, some are reserved for special purposes
  And, addresses are allocated in larger blocks
And, many devices need IP addresses
  Computers, PDAs, routers, tanks, toasters, …
Long-term solution: a larger address space
  IPv6 has 128-bit addresses (2128 = 3.403 × 1038)
Short-term solutions: limping along with IPv4
  Private addresses
  Network address translation (NAT)
  Dynamically-assigned addresses (DHCP)

## Slide 17: Hard Policy Questions
How much address space per geographic region?
  Equal amount per country?
  Proportional to the population?
  What about addresses already allocated?
Address space portability?
  Keep your address block when you change providers?
  Pro: avoid having to renumber your equipment
  Con: reduces the effectiveness of address aggregation
Keeping the address registries up to date?
  What about mergers and acquisitions?
  Delegation of address blocks to customers?
  As a result, the registries are horribly out of date

## Slide 18: Packet Forwarding
How hosts and routers forward IP packets ?

## Slide 19: Hop-by-Hop Packet Forwarding
Each router has a forwarding table
  Maps destination addresses…
  … to outgoing interfaces
Upon receiving a packet
  Inspect the destination IP address in the header
  Index into the table
  Determine the outgoing interface
  Forward the packet out that interface
Then, the next router in the path repeats
  And the packet travels along the path to the destination

## Slide 20: CIDR Makes Packet Forwarding Harder
There’s no such thing as a free lunch
  CIDR allows efficient use of the limited address space
  But, CIDR makes packet forwarding much harder
Forwarding table may have many matches
  E.g., table entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 21: Longest Prefix Match Forwarding
Forwarding tables in IP routers
  Maps each IP prefix to next-hop link(s)
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
  Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
Serial0/0.1
outgoing link

## Slide 22: Simplest Algorithm is Too Slow
Scan the forwarding table one entry at a time
  See if the destination matches the entry
  If so, check the size of the mask for the prefix
  Keep track of the entry with longest-matching prefix
Overhead is linear in size of the forwarding table
  Today, that means 450,000-500,000 entries!
  And, the router may have just a few nanoseconds
  … before the next packet is arriving
Need greater efficiency to keep up with line rate
  Better algorithms
  Hardware implementations

## Slide 23: Patricia (Radix, Trie) Tree
Store the prefixes as a tree
  One bit for each level of the tree
  Some nodes correspond to valid prefixes
  ... which have next-hop interfaces in a table
When a packet arrives
  Traverse the tree based on the destination address
  Stop upon reaching the longest matching prefix
0
1
00
10
11
100
101
00*
0*
11*

## Slide 24: Where do Forwarding Tables Come From?
Routers have forwarding tables
  Map prefix to outgoing link(s)
Entries can be statically configured
  E.g., “map 12.34.158.0/24 to Serial0/0.1”
But, this doesn’t adapt
  To failures
  To new equipment
  To the need to balance load
  …
That is where other technologies come in…
  Routing protocols, DHCP and ARP

## Slide 25: Host Forwarding Table
Command: netstat -r (Unix / Linux / Windows)
Destination Gateway Flags Ref Use Interface
-------------------- -------------------- ----- ----- ------ ---------
127.0.0.1 127.0.0.1 UH 0 26492 lo0
192.168.2. 192.168.2.5 U 2 13 fa0
193.55.114. 193.55.114.6 U 3 58503 le0
192.168.3. 192.168.3.5 U 2 25 qaa0
224.0.0.0 193.55.114.6 U 3 0 le0
default 193.55.114.129 UG 0 143454

## Slide 26: How Do End Hosts Forward Packets?
End host with single network interface
  PC with an Ethernet link
  Laptop with a wireless link
Don’t need to run a routing protocol
  Packets to the host itself (e.g., 1.2.3.4/32)
    Delivered locally
  Packets to other hosts on the LAN (e.g., 1.2.3.0/24)
    Sent out the interface
  Packets to external hosts (e.g., 0.0.0.0/0)
    Sent out interface to local router (gateway)
How this information is learned
  Static setting of address, subnet mask, and gateway
  Dynamic Host Configuration Protocol (DHCP)

## Slide 27: What About Reaching the End Hosts?
How does the last router reach the destination?
Each interface has a persistent, global identifier
  MAC (Media Access Control) address
  Burned in to the adaptors Read-Only Memory (ROM)
  Flat address structure (i.e., no hierarchy)
Constructing an address resolution table
  Mapping MAC address to/from IP address
  Address Resolution Protocol (ARP)
host
host
host
LAN
...
router
1.2.3.4
1.2.3.7
1.2.3.156